## Slide 1: CCP Module Programming Capture, Compare and PwM
PIC18f452

## Slide 2: INTRO
The CCP module (Capture/Compare/PWM) is a peripheral which allows the user to time and control different events.
CAPTURE - The contents of the 16 bit timer, upon detecting an nth rising or falling edge, is written to internal registers
COMPARE - Generate an interrupt, or change on output pin, when Timer 1or 3 matches a pre-set comparison value
PWM can generate signals of varying frequency and duty cycle on one or more output pins

## Slide 3: Intro
TWO CCP modules in PIC18f452  CCP1 & CCP2
Each CCP module contains a 16-bit register which can operate as a:
  • 16-bit Capture register
  • 16-bit Compare register
  • PWM Master/Slave Duty Cycle register
Registers associated with CCP1
  CCP1CON (8-bit)
  CCPR1 (16-bit)  Divided in two 8-bit regs (CCPR1L, CCPR1H)
  CCP1IF flag in PIR1 register
Registers associated with CCP2
  CCP2CON (8-bit)
  CCPR2 (16-bit)  Divided in two 8-bit regs (CCPR2L, CCPR2H)
  CCP2IF flag in PIR2 register

## Slide 4: CCP MODE – TIMER RESOURCE
NOTE: See T3CON register setting from datasheet

## Slide 5: Lets DISCUSS COMPARE MODE!

## Slide 6: COMPARE MODE
In compare mode, the 16-bit CCPRxH:CCPRxL register value is continuously compared against either with TMRlH:TMR1L or the TMR3H:TMR3L register pair value.
When a match occurs, one of the following actions may occur on the associated CCPx pin:
  Driven high
  Driven low
  Toggle output
  Remains unchanged
  Trigger a special event with hardware interrupt and clr the timer
In Compare Mode these settings are necessary.
  CCPx pin must be configured as output.
  TIMRER-1 or 3 must operate as timer or synchronous counter.

## Slide 7: INSIDE CCPxcon Register
bit 7-6 Unimplemented: Read as '0‘
bit 5-4 DCxB1:DCxB0: PWM Duty Cycle bit1 and bit0
Capture mode: Unused
Compare mode: Unused
PWM mode: These bits are the two LSbs (bit1 and bit0) of the 10-bit PWM duty cycle. The upper eight bits(DCx9:DCx2) of the duty cycle are found in CCPRxL.

## Slide 8: INSIDE CCP1con/CCP2CON Register
bit 3-0 CCPxM3:CCPxM0: CCPx Mode Select bits
0000 = CCPx module is off
0001 = Reserved
0010 = Compare mode, toggle output on match (CCPxIF bit is set)
0011 = Reserved
0100 = Capture mode, every falling edge
0101 = Capture mode, every rising edge
0110 = Capture mode, every 4th rising edge
0111 = Capture mode, every 16th rising edge
1000 = Compare mode,
Initialize CCP pin Low, on compare match force CCP pin High (CCPIF bit is set)
1001 = Compare mode,
Initialize CCP pin High, on compare match force CCP pin Low (CCPIF bit is set)
1010 = Compare mode,
Generate software interrupt on compare match (CCPIF bit is set, CCP pin is unaffected)
1011 = Compare mode,
Trigger special event (CCPIF bit is set)
Special Event in this case:: For CCP1 – Reset Timer value, For CCP2 Start ADC
11xx = PWM mode

## Slide 9: Compare MODE coding steps
Load CCPxCON reg for compare mode
Set CCPx pin as output
Load T3CON register to select TIMER-1 or TIMER-3 as clk base for CCPx module
Initialize Timer1 or Timer3 values.
THEN start that timer
Clear flag
Wait for CCPxIF
to become high
Goto next step according your requirement
Initialize CCPR1H:CCPR1L registers

## Slide 10
Scenario: Assume 1 Hz pulse is connected to Timer3 pin (T1CKI) and an LED is connected to RC2/CCP1 pin. Timer3 is being used as a counter. Using compare mode write code to toggle LED every 10 pulses
SOLUTION:
#include <p18F452.h>
void main (void)
{
CCP1CON = 0x02; // compare mode, toggle upon match
T3CON = 0x42; //timer 3 for compare, prescaler=1, external clk, SYNC on
TRISC.TRISC2 = 0; // configure CCP1 pin for output
TRISC.TRISC0 = 1; // T1CKI as input to use timer3 as counter
while(1)
{
CCPR1L=10; //initialize CCPR1 regs for 10 pulses
CCPR1H=0;
TMR3H=0;
TMR3L=0;
T3CON.TMR3ON=1; //start timer 3
while (PIR1.CCP11F==0); // wait for match i.e wait for 10 pulses
//CCP will automatically toggle CCPx pin
T3CON.TMR3ON=0; //off timer 3
PIR1.CCP11F = 0; //clr flag
}
}

## Slide 11: Lets DISCUSS CAPTURE MODE!

## Slide 12
CAPTURE MODULE
In Capture mode, CCPRxH:CCPRxL captures the 16-bit value of the TIMER-1/3 register when an event occurs on pin CCPx. An event is defined as one of the following:
  Every falling edge (1 » 0) on the CCPx pin.
  Every rising edge (0 » 1) on the CCPx pin.
  Every 4th rising edge (0 » 1) on the CCPx pin.
  Every 16th rising edge (0 » 1) on the CCPx pin
In Capture Mode these settings are necessary.
  CCPx pin must be configured as input.
  TIMRER-1 or 3 module must operate as timer or synchronous counter.

## Slide 13: INSIDE CCPxcon Register
bit 7-6 Unimplemented: Read as '0‘
bit 5-4 DCxB1:DCxB0: PWM Duty Cycle bit1 and bit0
Capture mode: Unused
Compare mode: Unused
PWM mode: These bits are the two LSbs (bit1 and bit0) of the 10-bit PWM duty cycle. The upper eight bits(DCx9:DCx2) of the duty cycle are found in CCPRxL.

## Slide 14: INSIDE CCP1con/CCP2CON Register
bit 3-0 CCPxM3:CCPxM0: CCPx Mode Select bits
0000 = CCPx module is off
0001 = Reserved
0010 = Compare mode, toggle output on match (CCPxIF bit is set)
0011 = Reserved
0100 = Capture mode, every falling edge
0101 = Capture mode, every rising edge
0110 = Capture mode, every 4th rising edge
0111 = Capture mode, every 16th rising edge
1000 = Compare mode,
Initialize CCP pin Low, on compare match force CCP pin High (CCPIF bit is set)
1001 = Compare mode,
Initialize CCP pin High, on compare match force CCP pin Low (CCPIF bit is set)
1010 = Compare mode,
Generate software interrupt on compare match (CCPIF bit is set, CCP pin is unaffected)
1011 = Compare mode,
Trigger special event (CCPIF bit is set)
11xx = PWM mode

## Slide 15: CAPTuRE MODE coding steps
Load CCPxCON reg for capture mode
Set CCPx pin as input
Load T3CON register to select TIMER-1 or TIMER-3 as clk base for CCPx module
Configure and Start Timer1 or Timer3.
Clear flag
Wait for CCPxIF
to become high
(wait for event)
Goto next step according your requirement
Read CCPRxH:CCPRxL registers if needed!
Initialize CCPRxH:CCPRxL registers

## Slide 16
SCENERIO: A switch is attached with CCP1 pin. Write a Program to throw TIMER1 values to PORTB ,PORTD and toggle LED attached with RA0 whenever a rising edge is detected on RC2/CCP1 through a switch.?
Solution:
void main() { ADCON1 = 0x07; // make all digital
TRISB=0; //PORTB to show timer value
TRISD = 0; TRISA.TRISA0=0; //LED TRISC.TRISC2=1; //CCP1 pin as Input
//CCP1 MODULE INITIALIZATION
CCP1CON = 0b00000101; // capture mode for every rising edge
CCPR1L=0; //initialize CCP1 regs
CCPR1H=0;
T3CON = 0x80; // Timer-1 for CCP1, Prescaler=1, Timer3 off T1CON = 0b10000000; // Prescaler=1, Timer1 off , Internal CLK, Sync off
TMR1H = 0; //initialize timer vlaues
TMR1L = 0;
T1CON.TMR1ON=1; //start timer 1
while(1) {
while(PIR1.CCP1IF == 0); // wait for rising edge on RC2/CCP1 PORTA.RA0 =~ PORTA.RA0; //toggle LED
PORTB = CCPR1H; //throw captured timer-1 value to PORTS
PORTD=CCPR1L; PIR1.CCP1IF = 0;
//write some lines here if I want to chk timer overflow and initialize it again } }

## Slide 17: Applications of Capture Mode
EVENT ARRIVAL TIME RECORDING. Some applications (e.g., a swimming competition) need to compare the arrival times of several different swimmers. The capture function is very suitable for this application. The number of events that can be compared is limited by the number of capture channels.
PERIOD MEASUREMENT. To measure the period of an unknown signal, the capture module should be configured to capture the timer values corresponding to two consecutive rising or falling edges, as illustrated in Figure

## Slide 18: Applications of Capture Mode
PULSE-WIDTH MEASUREMENT. To measure the width of a pulse, two adjacent rising and falling edges are captured, as shown in Figure
DUTY CYCLE MEASUREMENT. The duty cycle is the percentage of time that the signal is high within a period in a periodic digital signaL The measurement of duty cycle is illustrated in Figure

## Slide 19
Scenerio: Time Period Measurment of a pulse
Problem:Use the CCP channel 1 in capture mode to measure the period of an unknown signal, assuming that the PIC18 microcontroller is running with a 10-MHz crystal oscillator. The period of the unknown signal is shorter than 65536 clock cycles.
SOLUTION: The user needs to capture either two consecutive rising or falling edges and calculate their difference in order to measure the period.
void main (void)
{
unsigned int period;
CCP1CON = 0x05; // capture on every rising edge
T3CON = 0x80; //Timer1 for capture
TlCON = 0x80; //enable 16-bit timer1, prescaler =1, Clk internal
TRISC.TRISC2 = 1; // configure CCP1 pin for input
while(1)
{
CCPR1L=0; //initialize CCP1 regs
CCPR1H=0;
TMR1H=0; //initialize timer value
TMR1L=0;
PIR1.CCP11F = 0; //optional but its good to do it
while (PIR1.CCP11F==0); // wait for 1st rising edge
T1CON.TMR1ON=1;
PIR1.CCP11F = 0; //clr CCP for next edge
while (!PIR1.CCP11F); //wait for the 2nd rising edge
T1CON.TMR1ON=0; //stop timer 1
period = CCPR1;
CCP1CON = 0x00; //disable CCP1 capture
//write a line here to get period in seconds or micro seconds
}}

## Slide 20: Assignment
Write Duty cycle measurement code of a pulse using CCP2 and display binary of that %age duty cycle on PORTB

## Slide 21: Lets DISCUSS PWM MODE!

## Slide 22: PWM Mode
Generate a waveform with certain frequency and duty cycle using 8-bit Timer2.
Registers used in PWM mode
  CCPRxL register along with 2 LSbs of the CCPxCON register (DCxB1:DCxB0) used to hold duty cycle value
  8-bit PR2 register used to hold period of pulse

## Slide 23: INSIDE CCPxcon Register
bit 7-6 Unimplemented: Read as '0‘
bit 5-4 DCxB1:DCxB0: PWM Duty Cycle bit1 and bit0
Capture mode: Unused
Compare mode: Unused
PWM mode: These bits are the two LSbs (bit1 and bit0) of the 10-bit PWM duty cycle. The upper eight bits(DCx9:DCx2) of the duty cycle are found in CCPRxL.
bit 3-0 CCPxM3:CCPxM0: CCPx Mode Select bits
11xx = PWM mode
Rest options were used in Capture and Compare mode

## Slide 24: INSIDE t2con Register
bit 7 Unimplemented: Read as '0‘
bit 6-3 TOUTPS3:TOUTPS0: Timer2 Output Postscale Select bits
0000 = 1:1 Postscale
0001 = 1:2 Postscale
•
•
1111 = 1:16 Postscale
bit 2 TMR2ON: Timer2 On bit
1 = Timer2 is on
0 = Timer2 is off
bit 1-0 T2CKPS1:T2CKPS0: Timer2 Clock Prescale Select bits
00 = Prescaler is 1
01 = Prescaler is 4
1x = Prescaler is 16
SOME FEATURES OF TIMER2
8-bit timer (TMR2 register)
8-bit period register (PR2)
Interrupt on TMR2 match of PR2
The Timer2 module has an 8-bit period register, PR2. Timer2 increments from 00h until it matches PR2 and then resets to 00h on the next increment cycle.
PR2 is a readable and writable register. The PR2 register is initialized to FFh upon RESET

## Slide 25: PWM Period and DUTY Cycle Formulas
PWM PERIOD
The output pulse period (T) is determined by the PR2 register of the timer TMR2. The PWM period can be calculated using the following equation:
PWM Period = (PR2 +1) * 4Tosc * TMR2 Prescale Value.
So value for PR2 register that we have to load would be
e.g for Xtal=32Mhz, and Fpwm=10Khz, Prescaler= 4
PR2 = [(32 * 106 )/(10*103 * 4 * 4 )]- 1 = 199
PR2 = [Fosc/(Fpwm * 4 * PrecalerValue)]-1

## Slide 26: PWM Period and DUTY Cycle Formulas
PWM DUTY CYCLE
The PWM duty cycle is specified by using in total of 10 bits: eight MSbs of the CCPRxL register and two additional LSbs of the CCPxCON register (DCxB1:DCxB0). The result is a 10-bit number contained in the formula:
Pulse Width = (CCPRxL:DCxB1,DCxB0) * Tosc * TMR2 Prescale
DCxB9:DCxB0 = [Fosc/(Fdutycycle * PrecalerValue)]
Possible options of (DCxB1:DCxB0) bits Of CCPxCON register

## Slide 27: How to choose values of PR2 and CCP reg?
The lowest two bits (DC1B2:DC1B1) of the duty cycle in PWM Mode can be used to represent the fractional part (0.0, 0.25, 0.5, or 0.75) of the duty cycle value.
Calculate PR2 reg value from formula and then Choose CCPRxL as percentage of PR2 register.
E.g if PR2=50, and we need 20% duty cycle and then
CCPR1L=10 and DC1B1:DC1B0=00 (No decimal point)
because 20%*50=10.00
If we want 25% duty cycle for same PR2=50 then
CCPR1L=12 and DC1B1:DC1B0=10 i.e 0.5 division
because 25%*50=12.5
(12 in CCPR1L and 0.5 achieved by taking DC1B2:DC1B1 = 10)

## Slide 28: PWM MODE coding steps
Load CCPxCON reg for PWM mode. Take Care of DCxB1:DCxB0 bits
Set CCPx pin as output
Load T2CON register to select prescale value and clr TMR2 reg
Start Timer2
Clear Timer2 flag
Wait for TMR2IF
to become high
Goto next step according your requirement
Load PR2 reg to set PWM period
Set CCPRxL registers according to Duty Cycle

## Slide 29
PROBLEM: Write a program to create PWM with 75% duty cycle and with f=2.5khz, XTAL=10Mhz
SOLUTION:
void main()
{
CCP1CON=0; //reset CCP module , optional step
PR2=249; //using formula
CCPR1L=186; //75% duty cycle i.e 75%*PR2=186.75
TRSIC.TRISC2=0; //make PWM pin as output
T2CON=0x01; //Timer2, Prescaler 4 , No postscaler
CCP1CON=0x3C; //PWM mode , 11 for DC1B1:DC1B0 (0.75 fraction of CCPR1L)
TMR2=0; //clr timer reg
T2CON.TMR2ON=1; //start timer 2
while(1)
{
PIR1.TMR2IF=0; //clr timer flag
while(PIR1.TMRIF==0); // wait for end of period
}
}

## Slide 30: How it works? (page-601,602 of book)
When TMR2 value is equal to PR2
  TMR2 is cleared
  Pin RC2/CCP1 of PORTC is set high
  PWM duty-cycle byte loaded into CCPR1

## Slide 31
ASSIGNMENT:
Configure CCP1 in PWM mode to generate a digital waveform with 40% duty cycle and 10-KHz frequency assuming that the PIC18 microcontroller is running with a 32-MHz crystal oscillator.

## Slide 32: MikroC Library Functions for Pwm
PWM1_Init(constant long frequency) : This function initializes the PWM module with duty ratio 0. Frequency parameter is the desired frequency in Hz. It should be a numeric constant, should not be a variable.
PWM1_Set_Duty(unsigned short duty_ratio) : This function is used to set the duty cycle of the PWM. The parameter duty_ratio takes values from 0 to 255, ie 0 means 0% , 127 means 50% and 255 means 100% duty cycle. The PWM1_Init() routine must be called before using this.
PWM1_Start() : This function starts the PWM output. PWM1_Init() must be called before calling this routine,
PWM1_Stop() : This function stops the PWM output. PWM1_Init() must be called before calling this routine. PWM1_Start() should be called before calling this function otherwise calling this function will not have any effect as PWM module is not running.
NOTE: For microcontrollers with more than one CCP module, to use the desired CCP module for PWM generation simply change the number “1” in the prototype with desired module number. eg: PWM2_Init(5000), PWM2_Start().

## Slide 33
Self Explanatory Code:
In the below circuit four switches are provided for controlling the Duty Ratio of PWM generated by two CCP modules of the PIC Microcontroller.
Switch 1 : To increase the Duty Ratio of PWM produced by CCP1
Switch 2 : To decrease the Duty Ratio of PWM produced by CCP1
Switch 3 : To increase the Duty Ratio of PWM produced by CCP2
Switch 4 : To decrease the Duty Ratio of PWM produced by CCP2
Do By Yourself:
From code determine frequency and starting duty cycle of PWM??

## Slide 34
void main() //Mikro C code – Try to understand yourself
{
short current_duty_1 = 16; // initial value for current_duty_1
short current_duty_2 = 16; // initial value for current_duty_2
TRISD = 0xFF; // PORTD as input
TRISC = 0x00; // PORTC as output
PWM1_Init(5000); // Initialize PWM1
PWM2_Init(5000); // Initialize PWM2
PWM1_Start(); // start PWM1
PWM2_Start(); // start PWM2
PWM1_Set_Duty(current_duty_1); // Set current duty for PWM1
PWM2_Set_Duty(current_duty_2); // Set current duty for PWM2
while (1) // endless loop
{
if (!RD0_bit) // if button on RD0 pressed
{
Delay_ms(40);
current_duty_1++; // increment current_duty_1
PWM1_Set_Duty(current_duty_1); //Change the duty cycle
}
if (!RD1_bit) // button on RD1 pressed
{
Delay_ms(40);
current_duty_1--; // decrement current_duty_1
PWM1_Set_Duty(current_duty_1);
}
if (!RD2_bit) // if button on RD2 pressed
{
Delay_ms(40);
current_duty_2++; // increment current_duty_2
PWM2_Set_Duty(current_duty_2);
}
if (!RD3_bit) // if button on RD3 pressed
{
Delay_ms(40);
current_duty_2--; // decrement current_duty_2
PWM2_Set_Duty(current_duty_2);
}
Delay_ms(10); // slow down change pace a little
}
}